## Slide 1: RADIUS
RADIUS is a network protocol It is used to:
Verify users (authentication)
Allow or deny access
Record user activity
RADIUS checks whether a user is allowed to use the network or not.

## Slide 2: AAA
Authentication . Accounting
Checks username and password Records user activity: Answers: “Who is the user?” Login time,logout time
Authorization
Decides what access the user gets
Examples:
Only internet access
Admin access

## Slide 3: Components
Client (NAS – Network Access Server) . Database
Device that sends request Store information
Examples: User name ,password
Router Permissions
WiFi Access Point
RADIUS Server
Makes decision Allows or denies access

## Slide 4: Complete Working
WiFi Login
User enters username and password
Request Sent
Access Point creates a packet Sends Access-Request (RADIUS packet) Uses UDP port 1812
Server Verification
RADIUS server checks database
Server Response
Access-Accept → if correct
Access-Reject → if wrong

## Slide 5
Access Granted
User gets internet access
Accounting Starts
System records activity:
Accounting-Request (send data)
Accounting-Response (confirmation)
Records:
Login time
Data usage

## Slide 6
RADIUS Packets
RADIUS uses different message types:
Access-Request → Login request
Access-Accept → Allow access
Access-Reject → Deny access
Access-Challenge → Extra verification
Accounting-Request → Usage data
Accounting-Response → Confirmation

## Slide 7: Role of UDP
RADIUS uses UDP protocol
How it works:
Client creates packet
Sends via UDP (no connection setup)
Server replies using UDP
If packet is lost → it retries

## Slide 8: TACACS+ (Terminal Access Controller Access-Control System Plus)
TACACS+ is a network protocol that checks who a user is, controls what they can access, and records their activity mainly used for secure login and command control on routers and switches.
Admin tries to log in to a router.
TACACS+ checks the username and password.
Admin can see the settings but cannot delete them
“TACACS+ decides who can log in and what they are allowed to do.”

## Slide 9
Feature | RADIUS | TACACS+ | Example (Easy)
Protocol | UDP | TCP | RADIUS: Fast login to WiFi, no guaranteed delivery TACACS+: Admin logging into a Cisco router, reliable connection
Encryption | Partial (only password) | Full (everything encrypted) | RADIUS: Password secure, commands visible TACACS+: Entire session encrypted, commands safe
Main Use | Network access (WiFi, VPN, ISP) | Device/admin access (routers, switches) | RADIUS: Student login to WiFi TACACS+: Network admin login to router and run commands
Command Authorization | Limited | Detailed/Command-level | RADIUS: User can use internet, no control on actions TACACS+: Admin can “show config” but not “delete config”
Logging/Accounting | Yes | Yes, very detailed | RADIUS: Logs login/logout + data usage TACACS+: Logs every command admin executes
Speed | Fast | Slower than RADIUS (TCP) | RADIUS: Quick WiFi login TACACS+: Admin login slower but secure
Security | Medium | High | RADIUS: Password encrypted TACACS+: Everything encrypted including commands

## Slide 10
Thank you