## Slide 1
PROTOCOL
Address Resolution
Protocol (ARP)
Bridging the Gap Between IP Addresses and MAC Addresses
CEH | Ethical Hacking Essential Concepts · Module: Network Fundamentals

## Slide 2
What is ARP?
IP→MAC
IP to MAC Resolution
ARP maps a known IP address to an unknown MAC address — essential because devices on a LAN communicate via MAC, not IP.
BCAST
Broadcast Request, Unicast Reply
ARP sends a broadcast asking "Who has this IP?" Only the device with that IP replies directly (unicast) with its MAC address.
CACHE
ARP Cache
IP-to-MAC mappings are stored in an ARP table (cache) on devices, switches, and routers to avoid repeated broadcasts.
OSI Layer: Data Link (Layer 2) | Stateless: No connection tracking | RFC 826

## Slide 3
How ARP Works
SENDER
IP: 194.54.67.10 MAC: 00:1b:48:64:42:e4
NETWORK SWITCH
Broadcasts to all
TARGET (.3)
IP: 192.168.168.3 MAC: 00-14-20-01-23-47
STEP 1
→
ARP REQUEST (Broadcast): "Who has 192.168.168.3? Tell 194.54.67.10"
STEP 2
←
ARP REPLY (Unicast): "I am 192.168.168.3, my MAC is 00-14-20-01-23-47"
STEP 3
→
Connection Established — Sender stores MAC in ARP Cache

## Slide 4
ARP Packet Format
Byte 0
Byte 1
Byte 2–3
Hardware Type (2B)
Hardware Length (1B)
Operation Code (2B)
Sender Hardware Address — First 4 Bytes (MAC)
Sender HA — Last 2B + Sender PA — First 2B
Sender Protocol Address — Last 2B + Target HA — First 2B
Target Hardware Address — Last 4 Bytes
Target Protocol Address — 4 Bytes (IP)
Hardware Type
1 = Ethernet, 2 = Exp.Eth
Protocol Type
0x0800 = IPv4, 0x86DD = IPv6
Hardware Length
6 bytes (Ethernet MAC)
Protocol Length
4 bytes (IPv4 address)
Operation Code
1 = Request, 2 = Reply

## Slide 5
ARP Packet Encapsulation
ARP REQUEST
Null Destination MAC → Broadcast
Preamble +SFD 8B
Dest MAC 00:00:00:00:00:00 6B
Source MAC 0x645A04531E65 6B
Type 0x0806 2B
ARP Data 28 bytes 28B
CRC 4B
⚠ Destination = FF:FF:FF:FF:FF:FF (Broadcast)
ARP REPLY
Filled Destination MAC → Unicast
Preamble +SFD 8B
Dest MAC 0x645A04531E65 6B
Source MAC 0x0454530E2CAB 6B
Type 0x0806 2B
ARP Data 28 bytes 28B
CRC 4B
✔ Destination = actual MAC of requesting device (Unicast)

## Slide 6
ARP in Security — ARP Spoofing
How It Works
1
ARP has NO authentication — any device can send fake ARP replies.
2
Attacker sends a forged ARP reply: "I am 192.168.1.1, my MAC is AA:BB:CC:DD:EE:FF"
3
Victim updates its ARP cache with the attacker's MAC.
4
All traffic meant for the gateway now flows through the attacker.
5
This enables Man-in-the-Middle (MitM), sniffing, or Denial of Service attacks.
Countermeasures
Dynamic ARP Inspection (DAI)
Validates ARP packets against a DHCP binding table on managed switches.
Static ARP Entries
Manually configure critical IP-to-MAC mappings to prevent overwriting.
ARP Monitoring Tools
Tools like ARPwatch detect sudden ARP cache changes.
Encryption (TLS/HTTPS)
Even if sniffed, encrypted traffic can't be read by the attacker.
VLANs & Network Segmentation
Limit ARP broadcast domains to reduce attack surface.

## Slide 7
Key Takeaways
1
ARP resolves IP → MAC
Works at Layer 2, stateless protocol (RFC 826)
2
Broadcast → Unicast
Request is broadcast; reply is direct (unicast)
3
ARP Cache
Stored in devices, switches, routers to avoid re-querying
4
Packet = 28 Bytes
HW type, Protocol type, Length, OpCode, Addresses
5
No Authentication = Vulnerable
ARP Spoofing enables MitM, sniffing, DoS attacks
6
Defended by DAI + Static ARP
Dynamic ARP Inspection validates on managed switches
ARP — Address Resolution Protocol | Questions?